## Slide 1: Rotary endodontics
MDDr.Radovan Žižka

## Slide 2: Aim of seminary
Basic information about Ni-Ti alloy
Dividing NiTi rotary instruments
  Tip configuration
  Cross-sectional design
  Flute design
  Rake angle
  Taper
Principles o NiTi instruments
Fracture prevention of NiTi instruments
Techniques used with NiTi files

## Slide 3: NiTi alloy
1963 – developed for space program by Buehler at Naval Ordonance Laboratory
in Silver Springs, Maryland, USA
Very low elastic modulus (permit negotiation of curved canals)
Superelastic behavior
Shape memory

## Slide 4: Tip configuration
Cutting
  Transportation of canal in less experienced hands
  Making apical seal and obturation difficult
  Going long with it, creates an elliptical tear at the end of the root
Non cutting
  Reduces the risk of ledging,scratching or gouging
  Making apical seal and obturation easier
  Going long with it, creates concentric circle at the end of the root

## Slide 5: Cross sectional design
Triangular
Square
U shape
S type
Convex triangle
Proprietary ones

## Slide 6: Flute design part 1
Landed flute design(with radial lands)
  Cutting edges had been flattened (named radial lands), U-file design
  Instruments have to be pushed with light pressure to engage the perimeter of the canal and then cut the dentin there
  Make preparation slower but safer
  Increase strenght and decrease flexibility
  Good centering of instrument, preventing binding or screwing to dentin
Radial land
U shape

## Slide 7: Flute design part 2
Non-landed flute design
  Sharp cutting edges resulting from a traingular cross sectional design that cuts more rapidly but can lead also to preparation errors
  Consider more efficient but require more operator skill to avoid procedural mishap compared to radial-landed files
  More flexible
Others
Sharp cutting edge

## Slide 8: Rake angle
Is the angle formed by the cutting edge and a cross section taken perpendicular to the long axis of the instrument
Possitive rake angle
  Shave dentin
Negative rake angle
  Scrape dentin
Neutral rake angle
  Plan dentin

## Slide 9: Principles of NiTi part 1
Not use as pathfinder
Should not be used to negotiate small calcified canals or curved canals because of its non cutting tip
Should not be used to bypass ledges
Should not be applied with pressure
Should not be used for estimating working lenght (stainless steel instruments are more opaque)

## Slide 10: Principles of NiTi part 2
Need more flaring of access to decrease fatigue of file
Must be used in a lubricated canal to reduce frictional resistance
Should not be used in abrupt curves, S-shapes and canals that join
Once the instrument starts to wobble in the handpiece, the file should be disposed off

## Slide 11: Principles of NiTi part 3
When NiTi experiences any undue stress including cyclic fatigue, the metal undergoes a crystalline (microscopic) phase transformation and become structurally weaker
Cutting efficiency decreases with repeated sterilization(prone to fracture)
NiTi file may disarticulate without any warning especially if not properly used
Each instrument should not be used more than 5-10 secunds only

## Slide 12: Fracture prevention of NiTi rotary instruments part 1
Use only torque controlled handpiece
Establishing of proper glidepath
Use of crown-down technique
Frequent cleaning of flutes
Do not force the file apically against resistance
Remove the maximum possible pulp tissue with broach before using rotary files

## Slide 13: Fracture prevention of NiTi rotary instruments part 2
Canals should be well lubricated (no dentin mud which increase the risk of fracture)
Discard the file if it is bent, stretched, has shiny spots or wobbles in handpiece
Do not use rotary files to true working lenght especially in teeth with S-shaped canals, sharp curves
Frequently inspect file flutes under magnification

## Slide 14: Types of rotary instruments according to tapering
Tapered
  Constant - the diameter increases in a constant manner (Profile)
  Progressive - the diameter increases in a progressive manner (ProTaper)
  Variable - whether increaes in a variable manner (S1,S2) or increases then decrease (SX, finishing files)
Non-tapered

## Slide 15: Techniques that might be used for rotary instrumentation
Crown-down pressureless method
Modified crown down method
Graduating taper method
  Starting with smaller tapered instruments, where each instrument is taken to the full working lenght and then proceeding with larger tapers (tip size is constant)
Step-back method
Modified step-back method
  Use of Lightspeed system

## Slide 16: ProTaper
Is one of widely used NiTi system today
Innovations which characterize ProTaper:
  Progressive/variable taper
  Modified guiding tip(rounded, non-cutting and parabolic shaped tip)
  Varying tip diameters
  Convex triangular cross-section (not all of them)
  A positive rake angle
  Shorter handle of the file
  Work longer in superelastic phace than do instruments with U-file design

## Slide 17: ProTaper instruments
3 shaping and 3 finishing files (and 2 additional finishing files)
Shaping
  SX,S1,S2
Finishing
  F1,F2,F3
  F4,F5
http://www.dentsply.com

## Slide 18: ProTaper SX
SX File (auxiliary shaping file)
  Tip size – ISO19
  Taper -D0-D9 – from ISO 19-ISO 100
  -D9-D14 – from ISO100-ISO120 (reduction in taper to increase flexibility)
  Color code – none
  Designed to
      Coronal flaring
      Relocate the canal away from the external root concavities
http://www.dentsply.com

## Slide 19: ProTaper S1
S1 File
  Tip size – ISO18,5
  Taper - D0-D14 –
  from ISO 18,5-ISO 120
  (Increasibly larger taper)
  Color code – purple
  Designed to
      Preparation coronal 1/3 of root canal
http://www.dentsply.com

## Slide 20: ProTaper S2
S2 File
  Tip size – ISO20
  Taper - D0-D14 – from ISO 20-ISO 110
  (Increasibly larger taper)
  Color code – white
  Designed to
      Enlarge and prepare the middle 1/3 in addition to the critical coronal region of the apical 1/3
http://www.dentsply.com

## Slide 21: ProTaper F1
F1 File
  Tip size – ISO20
  Taper - D0-D3 – 7° taper
  - D3-D14 – a reduction in taper to increase flexibility
  Color code – yellow
  Designed to
      Primarily to finish apical 1/3 of the canal
      Expand the middle 1/3 of the canal
      Plane away the variations in canal diameter after shaping
http://www.dentsply.com

## Slide 22: ProTaper F2
F2 File
  Tip size – ISO25
  Taper - D0-D3 – 8° taper
  - D3-D14 – a reduction in taper to increase flexibility
  Color code – red
  Designed to
      Primarily to finish apical 1/3 of the canal
      Expand the middle 1/3 of the canal
      Plane away the variations in canal diameter after shaping
http://www.dentsply.com

## Slide 23: ProTaper F3
F3 File
  Tip size – ISO30
  Taper - D0-D3 – 9° taper
  - D3-D14 – a reduction in taper to increase flexibility
  Color code – blue
  Reduced cross-section with U-file design
  Designed to
      Same as F1 and F2
      Rigid and agressive
http://www.dentsply.com

## Slide 24: ProTaper
In addition there are F4 (double black, ISO40, initial taper is 6°) and F5 (double yellow, ISO50,initial taper is 5°)
Shaping instruments should be used in brushing motion, finishing with just light pressure
After each instrument irrigation,establishing patency and reirrigation

## Slide 25: ProTaper technique
Scout coronal 2/3 with K-file ISO 10, ISO 15 (coronal glidepath)
Shaping coronal 2/3 with S1,S2
Scout apical 1/3 with K-file ISO 10, ISO 15 – establishing working lenght (apical glidepath)
Finishing apical 1/3 with S1,S2,F1….

## Slide 26
http://www.dentsply.com

## Slide 27: Advantages of ProTaper part 1
Patented progressive taper design
Fewer files are needed to achieve fully tapered canal
Convex triangular section
  Increase the cutting efficiency
  Increase tactile sensation
  Decrease the lateral contact area between file and dentin
  Decrease torsional load, file fatigue and breakage

## Slide 28: Advantages of ProTaper part 2
The modified guiding tip can easily follow a prepared glidepath
A progressively changing helical angles and balanced pitches
  Stabilizing each instrument
  Aiding in debris removal
  Effectively reducing threading (screwing, grabbing and taper lock)

## Slide 29: ProTaper Next
http://www.dentsply.com