## Slide 1
TECHNIQUES AND METHODS OF PREPARATION OF ROOT CANALS
MDDr. Radovan Žižka

## Slide 2: AIM OF SEMINARY
Aim of endodontic treatment
Shaping and cleaning
  Schilder (1974)
  Contemporary aproach
Concepts which are used during root canal preparation
Techniques and methods of preparation of root canals

## Slide 3: AIM OF ENDODONTIC TREATMENT
Aim of endodontic treatment is desinfiction of root canal, which is followed by hermetic obturation

## Slide 4: SHAPING AND CLEANING
Shaping –the purpose is to prepare a shape of root canal which respects original anatomy and makes possible thorought cleaning and hermetic obturation
Cleaning – the purpose is to remove all the material in root canal (pulp, preparation debris, microorganisms)

## Slide 5: SHAPING AND CLEANING (Schilder,1974)
Shaping
  Mechanical aims
  Biological aims
Cleaning
  Exstirpation
  Dissolving material of biological origin
  Removing preparation debris

## Slide 6: SHAPING AND CLEANING (contemporary aproach)
Kompletní přístup
  Direct view on the whole pulp chamber floor and its morphology (root canal orifices)
  Straight line access
Continuously narrowing preparation
  Allows irrigation and removing of debris
  Allows hermetic obturation

## Slide 7: SHAPING AND CLEANING (contemporary aproach)
Respecting original anatomy
  Shape of root canal preparation respects and follow original anatomy
Protecting healthy teeth structures
  Increase resistance against fracture
  Decrease probability of perforation
  Apical preparation should be as small as it is possible to procede adequate cleaning

## Slide 8: CONCEPTS USED DURING PREPARATION
Straight line access (SLA)
Coronal flaring
Working lenght (WL)
Apical width (AW)
Patency
Recapitulation
Glidepath

## Slide 9: STRAIGHT LINE ACCESS
Ideally should working instrument reach foramen fysiologicum (or first curvature) without bending.
Influenced by:
    Shape of access cavity
    Coronal flaring

## Slide 10: CORONAL FLARING
Before we reach working lenght with ours instrument we should procede coronal flaring
  Remove the most infected tissue in root canal
  Create reservoir for irigation sollution
  Allows straight line access

## Slide 11: CORONAL FLARING
Gates-Glidden
Rotatory endodontic files
  ProTaper SX
  ProFile orifice shapers
Zdroje:
http://www.dentalcapitalbh.com.br/media/endodontia-maillefer/PROFILE-ORIFICE-SHAPER.jpg
http://t2.gstatic.com/images?q=tbn:ANd9GcRFzd64ffFlSVlBgqLeRkas-DSIzpjvIoBZFrX5AWN41mk1WcewZw
http://t2.gstatic.com/images?q=tbn:ANd9GcQ1pep7_AoQOTj-39l2cmMbqLtdv-GFWtwTb8lpgIgPjW0YnYD4

## Slide 12: WORKING LENGHT
Lenght of working instrument from reference point to foramen fysiologicum (boundary between cement and dentin)
Dentin
Cement
Pulp tissue
Foramen fysiologicum

## Slide 13: WORKING LENGHT
We can find it out
  Average values – very unprecise. Can be used only as safe lenght
  Radiologically – unprecise. Fysiological foramen is usually about 1-1,5 mm from anatomical apex
  Electronically– electronic apex locator (EAL) are based on pricipal that resistance between oral mucosa and periodontal ligaments is constant

## Slide 14: APICAL WIDTH
Depends on original diameter and shape of root canal, used taper of instrume and diagnosis
High taper
Less infected root canals
Small diameter(incisors, calcification)
Unpleasant root canal anatomy
Low taper
Badly infected root canal
Root canal retreatment
Bigger diameter(young patiens, palatal root of M1)

## Slide 15: PATENCY
Keeping apical foramen free of debris by using patency file (usually K-file size #10 or #15) that is passively extended just through apical foramen
Helps to maintain working lenght
Helps to removing preparation debris
Foramen fysiologicum
Foramen apicale
Patency file

## Slide 16: RECAPITULATION
Checking the working lenght with the working instruments with a 1ISO smaller diameter than working instrument we have used before
Helps to maintain working lenght
Helps to remove preparation debris

## Slide 17: GLIDEPATH
Using of (usually) stainless steel files before Ni-Ti rotarory files
Producing smooth reproducible glide path for rotatory instruments
    Preparation at least to ISO 15(allows removing preparation debris)
    Checking straight line access
    Valuable information abou root canal anatomy

## Slide 18: TECHNIQUES AND METHODS OF ROOT CANAL PREPARATION
Technique – instrumentation with one file
Method – instrumentation sequence (can obtain more techniques)
We divide to hand, rotatory,hybrid (following are hand ones)

## Slide 19: TECHNIQUES OF ROOT CANAL PREPARATION
Standarized (watch-winding)
Reaming
Filing
Balanced force

## Slide 20: STANDARDIZED TECHNIQUE
Indication
  Initial probing of root canal
  Recapitulation
  Retreatment
Complication
  Extrusion of preparation debris beyond apex
  Ledge
Instruments
  K-reamer, K-file

## Slide 21: STANDARDIZED TECHNIQUE
Instrument is pushing apically during rotating in clock-wise and anti clock-wise direction (about 45°)
15
15

## Slide 22: REAMING TECHNIQUE
Indication
  Straight root canals of circular diameter
Complication
  Straightening of root canals
  Zip-elbow
Instruments
  K-reamer (rotation 45°)
  K-file (rotation less than 45°)

## Slide 23: REAMING TECHNIQUE
We pass instrument passivelly to root canal and then we rotate it around 45° with small presure.Then we take the instrument out.
15

## Slide 24: FILING TECHNIQUE
Indication
  Oval shape root canals
  Retreatment
  Smoothing the preparation
Complication
  Extruding debris through apex
Instrument
  H-file

## Slide 25: FILING TECHNQUE
We insert instrument passivelly and then pull it up 2-3mm agains root canal wall. It´s neccesary to irigate very often and equal preparation of walls.
15

## Slide 26: BALANCED FORCE TECHNIQUE
Indication
  Complicated root canal anatomy
  The most universal technique for glidepath
Complication
  Straightening of root canal
Instrument
  K-flexofile (Flex-R file)
  K-file

## Slide 27: BALANCED FORCE TECHNIQUE STEP 1
Insert instrument passively which has 1ISO diameter larger than current master apical file.
15

## Slide 28: BALANCED FORCE TECHNIQUE STEP 2
With small pressure we rotate instrument around 90° in the clock-wise direction. Instrument will engage dentin of the root canal wall.
15

## Slide 29: BALANCED FORCE TECHNIQUE STEP 3
With minimal pressure we rotate instrument around 180-270° counter clockwise direction. Pressure should maintain instrument at or near the clockwise insertion depth. It will break loose the engaged dentin chips from root canal wall.
15

## Slide 30: BALANCED FORCE TECHNIQUE STEP 4
The file si then removed from root canal by a slow clockwise rotation around 360° that loads debris into the flutes and elevates is away.
15

## Slide 31: BALANCED FORCE TECHNIQUE STEP 4
Because we don´t use prebend files the straightening of root canal can occur. If root canal is complicated we suggest instead of step 4 go on with step 1 until the working lenght is reached. (ledge and breakage are more probable)

## Slide 32: METHODS OF ROOT CANAL PREPARATION
Apicocoronal – we prepara from begging with complete working lenght or we shorten it.
    Combined (reaming-filing)
    Step-back
Coronoapical – we prepare with shortened working lenght which is further prolonged.
    Step-down
    Double flared
    Crowndown presureless

## Slide 33: COMBINED METHOD
Indication
  Straight canals (oval)
  Recreation of apical stop after overinstrumentation of apex
Complication
  Zip-elbow, perforation (in case of curvature in apical part of root canal)
Instruments
  Changing of K-file and H-file

## Slide 34: COMBINED METHOD
By K-file we prepare with balanced force technique up to working lenght
Then passively insert H-file and with filing technique we prepare root canal
We repeat whole procedure with files 1 ISO larger.
15
15
20
20

## Slide 35: STEP-BACK METHOD
Indication
  Mediate to severe curved canals
Complication
  Reduction of their occurence
  Time demanding
Instruments
  In the past prebend H-file, these days are prefered K-files

## Slide 36: STEP-BACK METHOD
Main idea is continuous shortening the working lenght of instruments with larger diameter
It consists of two steps
  Preparation of apical stop
  Preparation of continuously widening taper

## Slide 37: STEP-BACK METHOD
Preparation of the apical stop which has adequate diameter at the correct working lenght ( for example ISO 35)
Next instrument is insterted to shortened working lenght (original working lenght – 0,5 mm) and preparation is repeated
In the end we prepare with master apical file to make root canal walls smooth
35
40
45
50
55
60

## Slide 38: STEP-DOWN METHOD
Indication
  Formerly invented for molards
  Mildly curved, rather oval root canals
Complication
  Reduction of occurence
  Time demanding
Instruments
  Combination of K-file, H-file, Gates-Glidden

## Slide 39: STEP-DOWN METHOD
Contains 3 steps
Aim is to:
  Determine working lenght which is constant
  Minimalize the possiblity of extrusion the debris throught apex
  Precise recognition of apical width

## Slide 40: STEP-DOWN METHOD
1.Step
Preparation of coronal 2/3 of root canal with filing technique (H-files ISO15,20,25), working lenght can be determined with ISO 8 instrument.
2/3
15
20
25

## Slide 41: STEP-DOWN METHOD
2.Step
Coronal flaring with Gates-Glidden (1-4), or ProTaper/ProFile
2/3

## Slide 42: STEP-DOWN METHOD
3.Step
Preparation to working lenght (min. ISO 35) with balanced force technique and followed by step-back technique

## Slide 43: DOUBLE FLARED METHOD
Indication
  Almost no restriction
Complication
  Reduction of occurence
Instruments
  K-file, Gates-Glidden

## Slide 44: DOUBLE FLARED METHOD
In fact it´s step-down method where the first step is missing. Thorought coronal flaring brings same advantages as with step-down method. In the same time is reduced possibility of extruding infection apically
Koronal flaring + step-back

## Slide 45: DOUBLE FLARED METHOD
1.Step
Coronal flaring with Gates-Glidden (1-4), či ProTaper/ProFile
2/3

## Slide 46: DOUBLE FLARED METHOD
2.Step
Preparation to working lenght(min. ISO 35) by balanced force technique and followed by step-back method

## Slide 47: CROWNDOWN PRESURELESS METHOD
Indication
  Curved root canals of round diameter
  Excellent shape of preparation
Complication
  Same occurence as with step-back and double flared methods
Instruments
  K-file

## Slide 48: METODA CROWNDOWN PRESURELESS
Working with no pressure
Determining working lenght (For example ISO 15)
Firstly we use instruments of larger diameters and rotate counter clockwise direction (we do not insert them to full working lenght) (For example from ISO 50)
15
50
45
40
35
30
25
20

## Slide 49: CROWNDOWN PRESURELESS METHOD
Then we would repeat whole sequence, this time with files of 1ISO larger diameter (For example now from ISO 55),so many to times, to obtain apical width which is desired
This method is used by the most of rotatory endodontic systems

## Slide 50
Thanks for attention